## Slide 1: Final Presentation Task 4: Market-based task allocation with heterogeneous team of robots
Groupe 8
Jacques Benand
Lucas Maneff
Paul Richard
Introduction
Centralized
Distributed
Conclusion
Notes: Welcome !

## Slide 2: Introduction : World and Scenario
Centralized
Distributed
Conclusion
Introduction
Natural Disaster with several victims :
Medical treatment ⇒ Task A: Red
Psychological support ⇒ Task B: Bleu
Fleet of robot to assist them:
Specialized ( 2 task A, 3 task B)
2 min of energy
Goal :
Maximize assistance delivered in 3 min
Test multiple market based method
Notes: Présenter ou se situe la création d’un nouveau produit dans la chaîne générale d’une entreprise
Présenter l’exemple qu’on va suivre tout au long de la présentation
…
Chaque slide combinera théorie et exemple pratique pour illustrer le processus.

## Slide 3: Market Based Algorithm
Auction to find the best fit for a robot :
Centralized
Distributed
Conclusion
Introduction
 | Centralized | Distributed
Bid | Robots | Robots
Auction | Supervisor | Robots
Bid Calculation (same for all methods) :
Bid = Time to go to task + Time to do Task
rob 1 (A)
rob 4 (B)
1
1
3
8

## Slide 4: Contribution
Centralized
Distributed
Conclusion
Introduction
Centralized
Distributed
Lucas MANEFF
Paul RICHARD
Jacques BENAND
World set up
Slides and git

## Slide 5: Centralized
Centralized
Distributed
Conclusion
Introduction
Supervisor
Robots
Auction each task sequentially
Compute the bid
Announce the Auction to all robots
Assign the Task to the best bidder
Send it back to the supervisor
Do the task
Notify the winning robot

## Slide 6: Centralized
Centralized
Distributed
Conclusion
Introduction
 | Collision | Event Handled | Activation Time
Mean | 7 | 88.8 | 55.53 %
Std | 2.45 | 13.54 | 4.36 %

## Slide 7: Centralized multi step planning
Centralized
Distributed
Conclusion
Introduction
Supervisor
Robots
Create bundles of 3 tasks
Compute all the possible arrangements
Announce the bundle to all robots
Keep the best one
Assign the bundle to the best bidder
Bid on the bundle
Do all the assigned tasks
Send the task in the best order

## Slide 8: Centralized multi step planning
Centralized
Distributed
Conclusion
Introduction
 | Collision | Event Handled | Activation Time
Mean | 13 | 60.8 | 63.43 %
Std | 2.73 | 7.05 | 3.67 %

## Slide 9: Distributed
Centralized
Distributed
Conclusion
Introduction
Supervisor
Robots
Create new task
Send new task info to every robot
Task finished ?
Yes
Robot loop
No

## Slide 10: Distributed
Centralized
Distributed
Conclusion
Introduction
Robot loop
Compute the bid for each task
Compare the bids
Lowest bid ?
No
Claim task
Do the task
Task completed ?
Yes
Notify the supervisor
No
Yes
Inter-robot communication

## Slide 11: Distributed
Centralized
Distributed
Conclusion
Introduction
 | Collision | Event Handled | Activation Time
Mean | 14.4 | 71.8 | 62.68 %
Std | 2.06 | 6.68 | 4.10 %

## Slide 12: Distributed multi step planning
Centralized
Distributed
Conclusion
Introduction
Robot loop
Compute the bid for each task
Compare the bids
Lowest bid ?
No
Count number of lowest bids
Compute bid for every permutation of m tasks
Task completed ?
Yes
Notify the supervisor
No
Yes
Inter-robot communication
Go to first task of sequence with lowest bid

## Slide 13: Distributed multi step planning
Centralized
Distributed
Conclusion
Introduction
 | Collision | Event Handled | Activation Time
Mean | 18.8 | 80.60 | 64.61 %
Std | 4.26 | 5.50 | 4.67 %

## Slide 14: Conclusion
Centralized
Distributed
Conclusion
Introduction
 | Centralized | Centralized planned | Distributed | Distributed planned
Collision | 7 | 13 | 14.4 | 18.8
Event Handled | 88.8 | 60.8 | 71.8 | 80.6
Activation time | 55.53 % | 63.43 % | 62.68 % | 64.61 %

## Slide 15: Thank you for your attention !
To visualize the videos, please refer to the PDF presentation :)
Notes: Welcome !

## Slide 16: Centralized multi step planning
Centralized
Distributed
Conclusion
Introduction
Analysis
- Poor performance in terms of the number of tasks completed.
- Efficient energy usage by robots
- But sometimes leave 1-2 robots inactive (e.g., Robot 1 on the map).
New Idea (was not implemented)
- The supervisor auctions tasks sequentially and delegates optimization to the robots.
- Each robot:
- Rearranges its tasks to maximize efficiency (3-opt search).
- Bids based on the optimized task arrangement.